## Slide 1: Efficient Visual-Inertial Navigation using IMU Pre-integration
Liyang Liu 2016-05-13

## Slide 2: Visual-Inertial SLAM
Visual-Inertial
SLAM
IMU
gyroscope
Acceleromt’r
Camera
(mono/stereo)
Accurate map
+
Motion
Angular velocity B ω
Linear accel. Ba
~1000Hz
Images
~20Hz

## Slide 3
Graph SLAM revisited
What’s good parameterization of x, z
Naïve parameterization:
  x: pose, orientation, velocity {Rt, wpt, wvt } for all IMU samples
  z: all IMU data points {B ωt, Bat }, t [0 ~ Ttotal] and all feature observations {zil}, iItotal lCi Itotal: all frms; Ci : correspondences in frm i; B refers body frame
  : angular rate noise: ηg, linear acc noise: ηa, image uv noise: ηi
  Process model:
Infeasible: X
  too much observation data
  Re-compute integration for each new linearization point change (estimating new rotation Rt ).
ML (maximum likelihood) of state space
A constrained optimization problem: assuming Gaussian observation
Gauss-Newton Framework
Needs to linearize f(x), given:
Parameterization of x, z
f(x)
Jacobian( f(x) )
Σz

## Slide 4: Pre-integration on IMU -- New form of state space and observations
x: pose, orientation, velocity for all key frame times: {Rt, wpt, wvt }
z: Inertial delta -- integrated IMU data points (over key frame duration) {ΔRij, Δvij, Δp+ij }, i,j [adjacent keyframes] , delta rotation (Eq 1)
  , delta velocity due to acceleration (Eq 2)
  , corrective term to account for acceleration (Eq3)
New observation model z = f(x): (Eq 4) (Eq 5) (Eq 6)
Advantage:
  Initial orientation is world frame. No explicit initialization stage or large uncertainty prior required.
  Inertial observation integrated in body frame, K inertial observations treated as a single observation, reduces linearization error, Gauss-Newton more robust.
  Much reduced state space and observation size, less computation
  Can be implemented in real-time

## Slide 5: Σ Calculation in Pre-integration
Re-write (EQ1~3) to get pre-integration process model
(Eq7)
  (Eq8)
  (Eq9)
=0
, (Eq10)
(Eq11)
(Eq12)
Pre-integration in recursive form
Angular velocity
~ N ( B ω, )
Linear accel:
~ N ( B a, )
delay

## Slide 6: J Calculation in Pre-integration, from Eq4~6

## Slide 7: Estimation of IMU non-zero bias
B ωt, Bat consist of non-zero bias bg, ba(low pass) + gaussian noise ηg, ηa
Solution:
  assume bias is known, let = 0, i.e. is part of observation z;
  estimate , i.e. part of state vector x
  Previous integrtion stays, except updated with 1st order expansion
Rewrite (Eq7~9) as:
(Eq 13)
(Eq14)
  (Eq15)

## Slide 8: Final x, z, S,J for Pre-Integration Graph SLAM
  Observation preintegration z becomes : , i,j [adjacent frames]
  State vector becomes:
Covariance computed same way as (Eq10), A, B in (Eq11,12) are expanded ,
,
Jacobian for {ΔRij, Δvij, Δp+ij } over Rt, wvt, wpt same as before
Expand Jacobian for members over , , see below
Yet J can also be computed iteratively

## Slide 9: Experimental Results
Comparison of Naïve VIN vs Pre-integration
 |  | Naïve VIN | Preintegration
Num camera poses=10 | Num iterations | 1000 | 25
 | Total time | 1644.2 [sec] | 17.1[sec]
 | Result/mdx | Not convergent yet, Max(Δx) = 4.76 | Yes converged, Max(Δx) = 17.6
Num camera poses=20 | Num iterations | 1000 | 19
 | Total time | 3403 [sec] | 25.3 [sec]
 | Result/mdx | Not convergent yet, Max(Δx) = 7.64 | Yes converged, Max(Δx) = 3.87
Num camera poses = 150 | Num iterations | NIL | 17
 | Total time | NIL | 171.4 [sec]
 | Result/error2 | Rank defiicient | Max(Δx) = 11.3
Simulation results for 150 camera poses

## Slide 10: Reference
[1] T. Lupton and Sukkarieh, “Visual-Inertial-Aided Navigation for High-Dynamic Motion in Built Environments Without Initial Conditions”, IEEE Transactions on Robotics, 2012
[2] C. Forster, et. al, “IMU Preintegration on Manifold for Efficient Visual-Inertial Maximum-a-Posteriori Estimation”, Robotics: Science and Systems, doi:10.15607/rss.2015.xi.006
[3] C. Forster, et. Al., “Supplementary Material to IMU Preintegration on Manifold”, 2015. [Online]. Available : http:// rpg.ifi.uzh.ch/docs/RSS15_Forster_Supplementary.pdf